# Architecture and Design of the TANGO device server for the Power supplies at ALBA

# Revisions
# Introduction
At ALBA a variety of different power converters for different purposes including Di-, Quad- and Sextupoles for booster and storage ring, over the corrector magnets to the power supplies of the ID. While the power converters differ widely in their specific use and the functionality provided, nearly all provide all current and voltage read back and many share common traits. In addition the ALBA power supplies DS includes abstract that account for differences between the current set in the power supply and the current effective at the magnet. This document tries to describe the generic TANGO interface used at ALBA.
Date	Version	Change	By
9. February 2009	0.1

# Types of Powersupply
## Basic Current Regulation
- Dipoles (Bending)
- Sextupoles (Chromacity)
- Quadrupoles (Focusing)
## Fast Current Regulation
- Corrector Magnets
- Skew Correctors
- Trim Coils (very precise tuning)
- Insertion Devices
## Ramped for the Booster
- Dipoles
- Sextupoles
- Quadrupoles
- Correctors
## Pulsed (Kicker and Septums)
Linac Injection Kicker
- Booster Extraction Septum
- Booster Injection Septum
- Storage Ring Injection Kicker
- Storage Ring Injection Septum
## Ramped
for the RF Cavities

# PCs by System
## Linac to Booster Transferline
Magnet	Type	Use	DS
Dipole	slow	Bending	BrukerEC1_PC
Qudrupoles	slow	Focussing	BrukerEC1_PC
Corrector	fast	correcting	BrukerALC_PC
Kicker	pulsed	Kicking	PPT_PC

## Booster
Magnet	Type	Count	Location	DS
Kicker	pulsed			PPT_PC
Dipole	ramped	1 ?		BrukerEC1_PC
Qudrupoles	ramped			BrukerEC1_PC
Sextupoles	ramped	Individually		BrukerEC1_PC
Corrector	fast	10+2 ?		BrukerEC1_PC
Kicker	[ulsed			PPT_PC

## Booster to Storage Ring Transferline
Magnet	Type	DS
Dipole	slow	BrukerEC1_PC
Qudrupoles	slow	BrukerEC1_PC
Corrector	fast	Bruker_PC_Phoenix
Kicker	pulsed	PPT_PC

## Storage Ring
Magnet	Type	Count	Location	DS
Septum	pulsed			PPT_PC
Dipole	slow	1 family	SR15	Hazemeyer_PC
Qudrupoles	slow	individual	per sector	Hazemeyer_PC
Skew	Slow			Hazemeyer_PC
Sextupoles	slow	9 Families	SR15	Hazemeyer_PC
Corrector	fast			PSI_PC
Corrector for ID	fast			PSI_PC
Trim Coils	fast			PSI_PC
RF	AC

## DS for Power Supplies
DS	Engineering Contact	Interface	Deadline
BrukerEC1_PC	Roberto Petrocelli	Custom protocol (BCEC1?)	30 February
BrukerALC_PC	RP / MT?	Modbus over TCP (ALBA_PLC)	7. March (5 days)
Hazemeyer_PC	Miquel Teixido	Modbus over TCP (ALBA_PLC)	3rd February
PSI_PC	Roberto	Custom Serial and F/O	ready
PPT_PC	Montse?	proprietary ASCII over TCP/IP	prototype

PC GUI update			4th Feb
PC GUI for PPT
Waveform Bench
power supply Testing Suite			5th Feb
LT+Booster names			6th Feb

# Requirements
While the majority of the device servers that control the power converters are simple but used in day to day operation and should run for extended periods without failure. Therefore the following aspects must be handled with special care.
- Memory Management: The device server must not leak memory, or file descriptors or other resources, in particular when handling exceptions or when calling Init.
- Error Handling: If an error occurs it shall be handled gracefully, that is other resources shall stay unaffected by startup, shutdown and error condition in the device server.
- Transparent Reconnection: If the connection to the power supply fails it the device server shall keep running and reestablish the connection when possible.
- Starting Gently: The restart of the DS should not affect the state of the power supply.
# Current Adjustment
It must be possible to adjust the Current value of all PCs to make up for two kinds of error:
1. imprecision from PC hardware
2. inaccuracies of magnet
3. positioning errors.
4. tune correction
We decided that employ a linear adjustment.
Short	Name	Description	Type
Iset	CurrentSetpoint	Ideal current setting, without taking offsets and scaling factors in account. / Writing this attribute WILL affect TANGOs CurrentReference write value.	RW attribute
o	CurrentOffset	Offset that will be added to current setpoint. Writing this attribute WILL affect TANGOs CurrentReference write value.	RW attribute
f	CurrentFactor	Factor for scaling (Iset+o)	property
Iref	CurrentReference	Reference current finally set on the hardware including the adjustments described above such as adding an offset. Writing to this attribute directly changes the reference current of the hardware, but does not affect TANGOs write current set point, offset(or scaling factor.	optional RW attribute
Imeas	CurrentMeasure	Raw current measured / read back from PC control unit, without any adjustments.	optional R-only
I	Current	Current read back as shown to the user.	R-only attribute

We will use the following formulas the different Current values.
Iref = f ( Ibase + o)
and
I = Imeas / f - o

.Voltage regulation will work strictly analogous.

# ALBA Power Converter Interface
## States
State	Color	Descriptions
INIT	Golden	Some form of initialization is done (init_device). Loading waveform.
ON	Green	Power active. / PPT Kicker high voltage enabled and pulser unit off..
OFF	Gray	PC does not supply power.
ALARM	Orange	Voltage or Current supplied significantly deviates from set point / Including supplying power when it should be off and not supplying power when in on state. Interlock triggered.
FAULT	Red	PC indicates a broken hardware, programming error detected or connection lost.
MOVING	Light Blue	Optional. Indicates that the power converter has not reached the target current but regulation loop is active, magnet is powered.
RUNNING	Light Blue	Ramping Mode for Ramped Power supplies.
STANDBY	Yellow	Optional. Precise meaning depends on the type of the power supplies, for the Hazemeyer it means that the power supply is ready to deliver Current but no reference setpoint was set.
UNKNOWN	DarkGray	Not Used.
DISABLE	Pretty in Pink	Not Used.

## Commands
Command name	Arg In	Arg Out	Comment
Init			(Re-)Initializes (and reconnects to) the device without otherwise affecting its state.
State		STATE
Status		STRING	Human readable presentation of the PC state.
On			Switches the Power Converter on. The current set point is applied to the current
Off			Switches the Power Converter off.
Standby			Optional, when supported. Switches the Power Converter to standby. If it was off before, the warm-up period phase begins. (optional, only if supported)
Command	STRING	STRING	(optional, expert) Sends the specified command to the device and reads its response. This is “cooked" and device dependent in the sense the special characters, that are common to all commands and hard to input to jive, such as line terminating characters, are appended automatically. Intended for such power supplies that employ a text based protocol.
ResetErrors			Resets error messages / interlocks.
Reset	-	-	Resets the control unit of the power supply back. The exact meaning depends on the control unit. Typically if the connection was lost, an attempt to reconnect will be made, the power supply will be switched off, errors will be cleared. (Although it is non-obvious when such a command would actually be used)
SipWaveform	-	-	Reads waveform from power supply hardware.
Depending on type of the power supply protocol, supplier more commands and attributes should be added.

Attributes	UNIT	Data Type	R/W Type
Status: Human readable, textual description of the device state. First line is designed to be shown in a synoptic view. / power on, current 1.9999 A / adjusting current 1.500 A, set point 2.000A / ramping current / ALARM: interlock bla bla / FAULT! no communication / off / on standby / loading waveform / warming up		String	R
Current: Current measured and read back from device, if supported. Note that Current must be a read-only attribute and CurrentSetpoint must be used to change the Current.	A	double	R
CurrentMeasure (Imeas) Raw current measured / read back from PC control unit, without any adjustments.	A	double	RO
CurrentSetpoint (Iset)The ideal Current setting in amps. To set the maximum current authorized by the power supply the attribute configuration will be used. Compare with Current attribute. This is before adjustment to make up for magnets and power supply variations. Mandatory for all power supplies with Current regulation. Setting Iset will change the TANGO write_value of CurrentReference attribute.	A	double	RW
CurrentReference (Iref) Current reference stored in power supply registers, after adjustment with CurrentOffset and CurrentFactor has been taken in account. (Expert). Changing this attribute will not affect the TANGO write_value of the CurrentSetpoint.	A	double	RW
CurrentTriggerMode Determines whether the Current set point is applied immediately when the CurrentSetpoint is written or the set point will be applied upon an external trigger.		short	RW
CurrentOffset (o) Offset added to current setpoint. Setting the current will update the TANGO write_value of CurrentReference attribute.	A	double
Voltage: The DC voltage that the PC currently supplies, in volts. Some DS will support writing but not all, the set point will be changed and applied when the On() command is executed. DS shall check whether a minimum and maximum is configured for this attribute. If not this it shall generate an error message and go back to the default state.	V	double	R
VoltageSetpoint (Uset) Setpoint for power supplies whose Voltage can be regulated such as the PPT Kicker power supplies.	V	double	RW
VoltageReference (Uref) Setpoint for power supplies whose Voltage can be regulated such as the PPT Kicker power supplies. (Expert)	V	double
VoltageTriggerMode Determines whether the Voltage set point is applied immediately when the VoltageSetpoint is written or the set point will be applied upon external triggers.		short	RW
VoltageOffset (p) Offset added to the VoltageSetpoint	V	double	RW
Resistance: (optional) Magnet resistance R = Voltage / Current			R
Errors: List of active error, faults and interlocks.		Array of Strings	R
RemoteMode: True if PC can be controlled remotely by this TANGO DS. False if in local mode, INVALID / not allowed, if the bit can not be read.		Boolean	R
Waveform: Used for ramping Booster power supplies. Read and Writing to this array will NOT trigger a new read / write from the power supply itself but access a buffer in the DS itself. The buffer updating will be handled by the DS itself, in the background. When writing this attribute another time, it will override the previous attempts, even while uploading. This allows the clients to remain responsive even when reading directly from the hardware would take exceedingly long time, and block the DS. Waveform uses its AttrQualities to signal its state of being loaded (CHANGING).The waveform is read when the DS is initalized and when DownloadingWaveform() is executed.		Array of double	RW
RampingMode Used to switch between ramping 1 and plain DC mode 0.		short	RW
Delta1 Iset - I		Double	R/O

Properties	Data Type	Default
Description Short description of the power supply type.	String
Name Name of the power supply as shown to the user. For example LT bending magnet	string
DocUrl Link to online documentation. Usually this will be a class property.	string
CurrentFactor: Scaling factor used in Currrent adjustment. (if any) See section above.	double	1.0
VoltageFactor Scaling factor used for Voltage adjustment (if any). See section above.	double	1.0
Decimation Controls how many data points are send to the power supply. When set to n only every nth data point will be send. Only for ramped power supplies.	integer	1